## Slide 1: Dance invaders
108062101張智孝 108062204 詹詠琪
A Four-Monitor Cabinet that echoes with the golden age of arcades

## Slide 2: GAMEPLAY dEMO

## Slide 3: TECHNICAL OVERVIEW

## Slide 4: DRIVING THE DANCEPAD
We were warned of the difficulty of connecting a USB dancepad to the FPGA, especially because the USB port on it has been overridden with a PS/2 emulator chip.
Very few open-source USB cores exist, and none that we’ve found are still actively supported.
Luckily, the USB dancepad we bought online uses the USB HID (Human Interface Device) specifications, meaning that its packets can be decoded easily like USB gaming joysticks.
Furthermore, we can easily serialize data from the computer into the FPGA using the UART port that the FPGA also uses to download bitstreams.
Using Allegro, we wrote a Dancepad Driver that translates the dancepad signals into UART byte-packets to be sent to the FPGA through a serial port.
A Digilent employee had written Verilog module for an UART receiver on the Basys3. To save time, we choose to adapt the module into our project and acknowledge credits to him.

## Slide 5: PARALLEL INTER-DEVICE TRANSMISSION

## Slide 6: IMAGE PRE-PROCessINg pt.1
We needed to use images in our project. In particular, the sprite images for the invading aliens.
The aliens’ image warp as they approach the boundaries of the screen, and grows bigger as they approach the player. Computing linear transformations on the aliens’ bitmap costs a huge amount of memory (to store intermediate buffers), making this idea quite infeasible. (Among other reasons)

## Slide 7: Image pre-processing pt.2
We chose instead to preprocess all the image transformations that we will use in the game and store it in one continuous block memory as Read-Only Memory.
(16 different distances) x (2-frame animation) x (4 horizontal transforms to approximate projection) x (2 different alien sprites) = 256 images to store!

## Slide 8: IMAGE compression pt.1
We employed a technique known as color quantization. In particular, for the aliens, we make it so every entry in the alien’s bitmap denotes whether it’s colored or not.
Furthermore, we took advantage of the symmetry in the sprites to only store the right half of every image.
All in all, a full sprite-set can be stored in around 300~kbits of memory. Had we stored every pixel entry in the 12-bit RGB format, we would hit over 3600k bits of memory usage, over twice the Basys3’s capacity.
The color quantization approach also gives us an additional advantage in that we can compute its color on-the-fly, allowing us to use palette changing to create 4 seemingly distinct aliens and adjust their color based on their distance.

## Slide 9: IMAGE compression PT.2
The method of color quantization is incredibly powerful, but conventional image-editing software does not support outputting in the form of pure binary.
Luckily, open-source libraries for image processing exists. We used the OpenImageIO library (along with Boost C++ for ease of coding) to process RGB/RGBA image formats (we’ve tried JPG and PNG). For the creation of the sprites, we used the web-application Piskel, and performed resizes through ImageMagick CLI commands. (With the help of shell scripts, of course)
Throughout development, we’ve experimented with output formats such as Xilinx’s binary coefficient files (.coe), SystemVerilog-applicable parameter header files (.svh), and space-separated binary readable through $readmemb. (.mem) We eventually settled with .coe as the final output, but for the ease of concatenating the binaries, we export as .mem first.

## Slide 10: Q&A

## Slide 11: THE END
HAPPY CHINESE NEW YEAR!